## Slide 1: g-factor measurement with cosmic muon and measurement of muonic X-ray
Kuno and Yamanaka Group Year-End Presentation 2017
December 28th 2017
Hasuike Daishin Miyamoto Koichiro
Nishikawa Ryo Ohta Saki

## Slide 2: content
g-factor measurement
Introduction
g-factor
Motivation
Cosmic muon
Charge ratio and polarization
Muon decay
Spin precession
Detection plan
How to identify muon?
Muon g-factor measurement
Design of the equipment & solenoid
Magnetic field distribution
Threshold determination
summery
Muonic X-ray measurement
Introduction
Motivation
Muonic atom and muonic X-ray
Semiconductor detector
Experiment
Selection of target
Setup
Design of target
What to do next
Summary
Back up

## Slide 3: Introduction g-factor
Compared to Hamiltonian
Therefore the value of g-factor is 2
Dirac particles follow the Dirac equation
From it we can obtain this

## Slide 4
But in reality, g-factor is not truly 2 because of quantum correction.
It called anomalous magnetic moment
Theoretical value 2.0023318361 ± 0.0000000010
Measured value 2.0023318414 ± 0.0000000012
The muon g-factor can be affected by physics beyond the Standard Model
High precision measurement is being done in all over the world
Of course , we can’t measure such a high precision, but we want to try it!
Notes: どこのデータか書く
いまやってる実験
そこまで精度は出せないけどやってみたい←motivation

## Slide 5: motivation
To measure muon g-factor with cosmic muon to the extend possible.
To increase accuracy twice as good as last year.
The value of g-factor measured last year
2.157±0.172
Reduce to half
Notes: 去年のデータ、改良予定点

## Slide 6: Cosmic muon
primary cosmic rays
π±,K± decay into μ±
positron
electron
π, K, γ, etc.
90% are proton
Abundance ratio
π：K1:9
Secondary cosmic rays

## Slide 7: Charge ratio and polarization
Charge ratio of atmospheric muons
1.28
Spin polarization ratio
P
Rest frame of π
laboratory frame
momentum
spin
100% polarized
Depending on the decay direction, the spin direction of μ reverses
Number of up spin muon
Number of down spin muon
or

## Slide 8: Muon decay
have negative charge
Mean life time
Capture by nuclei
Mean life time in copper
2.2μs
0.16μs

## Slide 9: Spin precession
In natural unit,
interaction Hamiltonian is
Think of ,
Schrödinger equation is given by
From this equation,
expected value can be calculated,
)
)
Therefore, spin precesses at angular velocity ω on xy plane
Notes: 歳差運動の図を入れる

## Slide 10
The electrons which come from muon decay are often go to the spin direction of muon.
The muons which stopped at the target in a magnetic field do spin precession, and released electrons through upper side or down side scintillator.
We measure B and ω
Last year measurement
We can calculate g-factor

## Slide 11
Detector(PMT)
Scintillatoｒ
Detection plan
How is the muon detected?
You can’t see it in your eyes...
Detect light signals by
PMT(PhotoMultiplier Tube)
when it goes through scintillators.
γ
Cosmic rays
Plastic scintillator
PMT
Source of pictures
PMT: https://www.hamamatsu.com/jp/ja/3001.html
Plastic scintillator: http://www.hep.sc.niigata-u.ac.jp/~vnd/
Notes: ミューオンをどうやって検出するのか？
目には見えない→シンチを通過した時の光信号をフォトマルで見よう

## Slide 12
How to identify the muon?
The muon penetrates scintillators easily, because it has heavier mass than other particles in the cosmic ray. So a signal detected by piled up scintillators is likely to be derived from the muon.
The muon decays to the electron and neutrinos with a mean lifetime of 2.2μs. If you detect a pair of signals with such an interval, there is a high possibility that you are seeing the decay event.
Cu plate
PMT C
PMT D
PMT A
PMT B
B
#2
stop
decay
D
#3
F
H
(2)
(2)’
Cherenkov counter
PMT E, G
PMT F, H
#1
(1)
*
* It’s just made of acrylic resin and no fluorescence. We couldn’t get enough scintillation counters.
What’s this?
Notes: ミューオンの判別方法
ミューオンは質量が大きく止まりにくいので、シンチを容易に貫通する。したがって、重ねたシンチでも検出できる信号はミューオンの可能性がある。
ミューオンは平均寿命2.2μsで電子とニュートリノに崩壊する。もしその間隔で一対の信号が検出できれば、ミューオンの崩壊事象を見ている可能性が高い。
#1: チェレンコフカウンタ ただのアクリル樹脂製で蛍光性はない。十分な数のシンチを用意できなかった。
#2,3: シンチレーションカウンタ
銅板（ストッピングターゲット）
#1と#2,3の間を空けることで、銅板に当たらないスタートトリガーの数を減らせる

## Slide 13
How to identify the muon?
(1)
(2)
OR
(2)’
Start trigger
Stop trigger
Interval=2.2μs
It’s the muon.

## Slide 14
Cu
S
scintillator
Muon g-factor measurement
Electrons after muon will be alternately detected by the upper and lower scintillators when putting the stopping target(Cu plate) into magnetic field.
→ g-factor can be obtained from the frequency of detecting cycle ω.
S
μ
B
scintillator
e
ω
Notes: 弱い相互作用におけるパリティ対称性の破れにより、電子はスピンと同じ方向に放出されやすい
スピンは磁気モーメントとともに回転するので、適切な磁場をかければ上下のシンチで交互に電子が検出される
→電子の検出周期からg因子が求められる

## Slide 15
Design of the equipment
 | Cerenkov counter | Scintillation counter | Cu plate
Length[cm] | 140 | 100 | 25
Width[cm] | 10 | 20 | 25
Height[cm] | 4 | 5 | 0.5×2 double-coursed
number | 2 | 2 | 6
Cerenkov counter
Scintillation counter
solenoid

## Slide 16
Design of the solenoid
We enlarged a solenoid to almost four times in order to adapt for the size of scintillators.
It also contributes to homogeneity of magnetic field.
 | Last year | This year
Length[cm] | 38 | 116
Width[cm] | 36 | 39
Height[cm] | 8 | 14
Number of turns | 340 | 1104
Current[A] | 5.002 | 5.00
Last year
This year
Notes: コイルの設計
シンチレータのサイズに合わせてコイルを大型化した
大型化は磁場の一様性にも寄与する

## Slide 17
Design of the solenoid

## Slide 18
Magnetic field distribution
Magnetic field intensity(unit: [G]) was measured using a Hall probe.
The intensity of the central magnetic field was determined based on the amount of current used in the experiment of last year.
Chart: Magnetic field distribution on the center line
| 11.6 | 34.8 | 58.0 | 81.2 | 104.4
 | 38.3 | 56.2 | 56.5 | 55.5 | 36.7

## Slide 19
Magnetic field distribution
38[cm]
B
Last year
116[cm]
B
This year

## Slide 20
Threshold determination
A histogram of the raw signal pulse height from PMTs was made using the following circuit, and the discriminator threshold was determined.
Simultaneous noise was excluded by setting the coincidence signal as trigger.
The threshold was set to the lowest level during this measurement.
Threshold determining logic circuit

## Slide 21
Threshold determination
0
Pulse height [mV]
-20
count
Histogram of raw signal pulse height
: raw signal
: trigger signal
noise
 | Applied voltage [V] | Threshold [mV] |  | Applied voltage [V] | Threshold [mV]
PMT A | 1790 | 500 | E | 2300 | 20
B | 1900 | 500 | F | 2100 | 20
C | 1865 | 500 | G | 2100 | 20
D | 1845 | 500 | H | 2100 | 20

## Slide 22
Summery
We want to try measuring muon g-factor with a cosmic ray.
The goal is to achieve twice the accuracy higher than last year.
The equipment is enlarged three times larger.
What to do next…?
Begin to take data with applying magnetic field
Error analysis and demonstration of its reduction
Solid angular last year×1/2
Size of target last year×3
Data taking time last year×1.5
uniformity of magnetic field last year×2
Total
halve the error

## Slide 23: Measurement of muonic X-ray with cosmic muons

## Slide 24: Motivation
●Recently, it seems to be popular to perform elemental analysis using muon in physical industry.
●We would like to touch cutting-edge research to the extent possible.
●It would be interesting that we can do element analysis with cosmic rays.

## Slide 25: Muonic atom
Atomic bound states formed by a negative muon and a nucleus
It takes sec to transition to the ground state
Bohr model

## Slide 26: Muonic X-ray
μ- is captured by an atom
Emit muonic X-rays with an energy level equivalent to the energy difference between the higher and lower states
The energy is characteristic to the element
Characteristic X-Ray Energies

## Slide 27: Operating principle of semiconductor detector
n : the number of electron-hole pair to be generated
E : the energy of radiation absorbed in semiconductor
ε : the required energy to generate a electron-hole pair
radiation
Depletion layer
Conduction band
Forbidden band
Valence band
metal
semiconductor
insulator

## Slide 28: Germanium detector
GMX20P4-70
●Advantage
・High energy resolution
●Disadvantage
・Cooling required

## Slide 29: Liquid Nitrogen
●Leave the underground laboratory immediately when there is an alarm.
●Don’t enter the lab room if the lamp near the door is lit.
●Please follow instruction of kuno lab staff when abnormality occurs.
（https://www.rex-rental.jp/anz/xo-326-2sa.htmlより参照）

## Slide 30: Selection of Target
We are satisfied if we can see the characteristic x-rays with cosmic rays.
It seems that aluminum is used as target in COMET.
Let’s experiment with the same as COMET.
Later, let’s see how the difference in purity contributes to the spectrum of x-ray.

## Slide 31: Setup
Amp
Dewar
Ge
MCA
Pre Amp
HV
target
X-ray
Ge
Scinti 1
Scinti 2
Scinti 3
target
trigger
X-ray
Scintillator size : 20cm×20cm

## Slide 32: Design of target
●Plan A
Ge
Al
●Plan B
Al
Ge
28cm
28cm
20cm
Y cm
20cm
X cm

## Slide 33: Design of target
Chart: Kinetic Energy of muon [MeV]
About Y
The larger Y is,
the better stop rate is.
(Roughly proportional relation)
About X
Al
Scinti 2
X and stop rate are proportional relations.
(X is up to 20cm,
because of scintillator size.)

## Slide 34: Design of target
About X
:mas attenuation coefficient
Intensity follows this formula
Chart: x [cm]
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0 | 12.0 | 13.0 | 14.0 | 15.0 | 16.0 | 17.0 | 18.0 | 19.0 | 20.0
 | 0.90484 | 0.81873 | 0.74082 | 0.67032 | 0.60653 | 0.54881 | 0.49659 | 0.44933 | 0.40657 | 0.36788 | 0.33287 | 0.30119 | 0.27253 | 0.2466 | 0.22313 | 0.2019 | 0.18268 | 0.1653 | 0.14957 | 0.13534
The intensity of x-rays emitted from the aluminum surface is 1.

## Slide 35: Design of target
About X
Chart: x [cm]
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0 | 12.0 | 13.0 | 14.0 | 15.0 | 16.0 | 17.0 | 18.0 | 19.0 | 20.0
 | 0.047601 | 0.09071 | 0.12975 | 0.16511 | 0.19714 | 0.22616 | 0.25244 | 0.27624 | 0.29781 | 0.31736 | 0.33506 | 0.35111 | 0.36565 | 0.37883 | 0.39078 | 0.40161 | 0.41143 | 0.42033 | 0.4284 | 0.43572
The greater X, the better.
So, X should be 20cm.
But, there is cost problem.
Notes: 20*20*3 7.8000円

## Slide 36: What to do next
●Measure efficiency of Ge detector.
●Perform energy calibration of MCA.
●Prepare target as soon as possible.

## Slide 37: Summary
●We wanted to see muonic x-rays with cosmic rays.
●We decided aluminum as the target.
●We thought about the shape of target.
●We have to get to the experiment early.

## Slide 38: Backup g-factor
Dirac particles follow the Dirac equation
Add the electromagnetic field、
Disassemble
Pauli-Dirac display

## Slide 39
Non-relativity approximation
(1)
(2)
Assign to (2)
Substitute for (1)

## Slide 40
Deforming the numerator
B : Magnetic flux density
finally
Compared to Hamiltonian
Therefore the value of g-factor is 2

## Slide 41
The electron distribution given by the V-A theory is
  Where
  is the angle of electron emission with respect to the muon polarization vector
  P is polarization ratio
Notes: グラフタイトル追加
式の部分改良

## Slide 42: Back up
Chart: x [cm]
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0 | 12.0 | 13.0 | 14.0 | 15.0 | 16.0 | 17.0 | 18.0 | 19.0 | 20.0
 | 0.95202 | 0.9071 | 0.86502 | 0.82557 | 0.78857 | 0.75385 | 0.72125 | 0.69061 | 0.66181 | 0.63471 | 0.60921 | 0.58518 | 0.56254 | 0.54119 | 0.52104 | 0.50201 | 0.48403 | 0.46703 | 0.45095 | 0.43572
厚さ | rate | intensity | ave int | rate*aveint
0 | 0 | 1 |  | 
1 | 0.05 | 0.951229 | 0.952022 | 0.047601
2 | 0.1 | 0.904837 | 0.907101 | 0.09071
3 | 0.15 | 0.860708 | 0.865018 | 0.129753
4 | 0.2 | 0.818731 | 0.82557 | 0.165114
5 | 0.25 | 0.778801 | 0.788572 | 0.197143
6 | 0.3 | 0.740818 | 0.75385 | 0.226155
7 | 0.35 | 0.704688 | 0.721246 | 0.252436
8 | 0.4 | 0.67032 | 0.690611 | 0.276244
9 | 0.45 | 0.637628 | 0.661809 | 0.297814
10 | 0.5 | 0.606531 | 0.634714 | 0.317357
11 | 0.55 | 0.57695 | 0.609208 | 0.335065
12 | 0.6 | 0.548812 | 0.585185 | 0.351111
13 | 0.65 | 0.522046 | 0.562543 | 0.365653
14 | 0.7 | 0.496585 | 0.54119 | 0.378833
15 | 0.75 | 0.472367 | 0.521039 | 0.390779
16 | 0.8 | 0.449329 | 0.50201 | 0.401608
17 | 0.85 | 0.427415 | 0.484031 | 0.411426
18 | 0.9 | 0.40657 | 0.467031 | 0.420328
19 | 0.95 | 0.386741 | 0.450948 | 0.4284
20 | 1 | 0.367879 | 0.435721 | 0.435721
Chart: Kinetic energy of muon [MeV]
| 5.0 | 10.0 | 15.0 | 20.0 | 25.0 | 30.0 | 35.0 | 40.0 | 45.0 | 50.0
 | 0.098208 | 0.33743 | 0.68808 | 1.1322 | 1.656 | 2.2485 | 2.9007 | 3.6052 | 4.3556 | 5.1464

## Slide 43: Contents
●Introduction
・Motivation
・Muonic atom and muonic X-ray
・Semiconductor detector
●Experiment
・Selection of target
・Setup
・Design of target
●What to do next
●Summary
●Back up